## Slide 1: 區塊圖形編輯設計

## Slide 2
基本概念複習

## Slide 3: Logic Gate Symbols and Behavior
Logic gates symbols:
Timing diagram(waveform)

## Slide 4: Logic Gates

## Slide 5: Expressions of Logic Function
Boolean equations, truth tables and logic diagrams describe the same function!
Truth tables are unique; equation and logic diagrams are not.
X
Y
F
Z
Logic Diagram
Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F
×
+
=

## Slide 6: Boolean Algebra
An algebraic structure defined on a set of at least two elements, B, together with three binary operators (denoted +, · and ) that satisfies the following basic identities:
1.
3.
5.
7.
9.
11.
13.
15.
17.
Commutative
Associative
Distributive
DeMorgan
’
s
2.
4.
6.
8.
X
. 1
X
=
X
. 0
0
=
X . X
X
=
0
=
X . X
10.
12.
14.
16.
X + Y
Y + X
=
(X + Y)
Z
+
X + (Y
Z)
+
=
X(Y +
Z)
XY
XZ
+
=
X + Y
X . Y
=
XY
YX
=
(XY)
Z
X(Y
Z)
=
X
+ YZ
(X + Y)
(X + Z)
=
X . Y
X + Y
=
X
+ 0
X
=
+
X
1
1
=
X + X
X
=
1
=
X + X
X = X

## Slide 7: K-Map
F(A, B, C, D) = ∑(0,1,2,4,5,6,8,9,12,13,14)
AB
CD
8
9
10
11
12
13
14
15
0
1
3
2
5
6
4
7
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
F(A, B, C, D) = A’B’C’D’+A’B’C’D+A’B’CD’+A’BC’D’+A’BC’D+A’BCD’+AB’C’D’+AB’C’D+ABC’D’+ABC’D+ABCD’
F(A, B, C, D) = C’+A’D’+BD’

## Slide 8
區塊圖形編輯設計

## Slide 9: 示範 F(A, B) = ∑(0,1,2)
F(A, B) = A̅ + B̅
F(A, B) = A̅B̅ +A̅B +AB̅
F(A, B) = ∑(0,1,2)
影片：https://www.youtube.com/playlist?list=PLuit3g1xQ3gJHvZWxLC8B5TEiIyISK84S

## Slide 10
課堂練習

## Slide 11: 實驗一 : Quartus操作練習
請完成下列邏輯表示並將以下檔案壓縮並上傳:
  專案
  Word 檔(電路設計截圖﹑模擬波形截圖)
  作業：F(A, B, C, D) = C’+A’D’+BD’
  加分：Y(A, B, C, D) = ∑(0,1,2,3,4,6,8,9,10,11,14)
  設計最簡電路圖

## Slide 12: 實驗一 : Quartus操作練習
作業：F(A, B, C, D) = C’+A’D’+BD’

## Slide 13: 實驗一 : Quartus操作練習
加分：Y(A, B, C, D) = ∑(0,1,2,3,4,6,8,9,10,11,14)